OceanSITES User’s Manual

NetCDF Conventions and Reference Tables

Version 1.2

December 7th, 2009

DRAFT

Table of contents

OceanSITES User’s Manual	1

1	OceanSITES data-management principles	6

1.1	About OceanSITES	6

1.2	About this document	6

1.3	OceanSITES data management structure and data access	6

1.4	User Obligations	6

1.5	Disclaimer	7

1.6	Further Information Sources and Contact Information:	7

2	OceanSITES NetCDF data format version 1.1	8

2.1	Data file dimensions	9

1.1.	Global attributes	9

2.2	Variables	13

2.2.1	Coordinate variables	14

2.2.2	Coordinate quality control variables	17

1.1.1	Data variables	17

3	OceanSITES metadata format	21

4	Reference tables	23

4.1	Reference tables 1: data type and data code	23

4.1.1	Reference table 1: Data type	23

1.2.	Reference table 2: Variable quality control flag scale	23

1.1.2	Reference table 2.1: Overall quality control procedure indicator	24

4.1.2	Reference table 2.2: cell methods	24

4.2	Reference table 3: OceanSITES parameter dictionary	25

4.2.1	Convention for parameter names, standard names and units	25

4.2.2	References	25

4.3	Reference table 4: Data Assembly Center Codes	27

1.3.	Reference table 5: data mode	28

4.4	Reference table 6: OceanSITES sites catalog	28

4.5	Reference table 7: sensor mount characteristics	29

4.6	Reference table 8: sensor orientation characteristics	30

5	GDAC organization	31

5.1	File naming convention	31

5.1.1	Data file naming convention	31

5.1.2	Example	32

5.1.3	Metadata file naming convention	32

5.2	Index file for data files	33

6	Glossary, definitions	35

6.1	SITE	35

6.2	PLATFORM	35

6.3	DEPLOYMENT	35

History

| Version | Date | Comment |
| --- | --- | --- |
| 0.1 | 20/03/2003 | TC: creation of the document |
| 0.3 | 20/02/2004 | TC: updates on locations, mooring name, data state indicator, parameters table, epic codes, history information |
| 0.3.2 | 26/05/2004 | N.G.: make more flexible, add dataset (metadata) file |
| 0.4 | 01/06/2004 | TC: separate data set description and data file, merge with Steve Hankins’s straw man |
| 0.6 | 28/06/2004 | TC: updates from Nan Galbraith, Steve Hankins, Jonathan Gregory, Brian Eaton |
| 0.7 | 23/05/2005 | Maureen Edwards: NOCS data centre, new GF3 parameters |
| 0.7 | 24/05/2005 | Roy Lowry: physical parameters from BODC Data Markup Vocabulary |
| 1.0 | 18/02/2006 | TC: updates following OceanSITES data management meeting 2006, Hawai’i §2.1: LEVEL dimension replaces DEPTH to accomadate depth or pressure §2.2: QC_MANUAL field created §2.2: CONVENTION field removed §2.2: PLATFORM_CODE added §2.2: SITE_CODE added §2.2: WMO_PLATFORM_CODE added §2.3: DEPTH renamed DEPH to comply to GF3 §2.3: DATA_MODE set at measurement level §3: metadata file description transferred to “OceanSITES metadata proposal” until approval §5: file naming convention updated |
| 1.0 | 19/02/2006 | NG: data codes in chapter 4.1.2 |
| 1.0 | 28/04/2006 | PF & NG: data mode optional |
| 1.0 | 28/04/2006 | TC & JG: §2.2 global attributes |
| 1.1 | April-May-June 2008 | NG, MM, TC, ML: general revision based on OceanSITES 2008 meeting Epic codes removed Use ISO8601 for string dates Remove general attributes Update global attribute section for CF-1.1 compatibility New dimensions for DEPTH, LATITUDE, LONGITUDE Add an uncertainty attribute New presentation of the document |
| 1.2 draft | September 2009 | §1.3 : GDAC distribute the “best data” statement §1.4 : add a “User obligations” paragraph §1.5 : add a “Disclaimer” paragraph §2 : note on format version §2.2.1 : no fill value allowed for TIME, LATITUDE, LONGITUDE, DEPTH §2.2.1 : use WGS84 datum for latitude and longitude §2.2.1 : DEPTH “reference” optional attribute §2.2.3 and §4.7 : use “sensor_mount” optional attribute §2.2.3 and §4.8 : use “sensor_orientation” optional attribute §2.2.3 : use sensor_name and sensor_orientation attributes §4.3 : revisit parameter names §4.4 : update DAC codes §4.6 : add a sentence on OceanSITES site naming policy §5.1 : new data file naming convention §5.2: add GDAC_CREATION_DATE, GDAC_UPDATE_DATE, PARAMETERS in the index file. |
| 1.2 draft | December 7th 2009 | §5.1: revisit file naming convention. §5.2: add a data_mode in the index file. §6: add a “Glossary, definition” chapter. |

# OceanSITES data-management principles

## About OceanSITES

The OceanSITES program is the global network of open-ocean sustained time series sites, called ocean reference stations, being implemented by an international partnership of researchers. OceanSITES provides fixed-point time series of various physical, biogeochemical, and atmospheric variables at different locations around the globe, from the atmosphere and sea surface to the seafloor. The program’s objective is to build and maintain a multidisciplinary global network for a broad range of research and operational applications including climate, carbon, and ecosystem variability and forecasting and ocean state validation.

All OceanSITES data are publicly available. More information about the project is available at: http://www.oceansites.org.

## About this document

The main purpose of this document is to specify the format of the files that are used to distribute OceanSITES data, and to document the standards used therein. This includes naming conventions, or taxonomy, as well as metadata content.

## OceanSITES data management structure and data access

The data flow within OceanSITES is carried out through three organizational units: PIs, DACs, GDACs.

The Principal Investigator (PI), typically a scientist at a research institution, maintains the observing platform and the sensors that deliver the data. He or she is responsible for providing the data and all auxiliary information to a Data Assembly Center (DAC).

The DAC assembles OceanSITES-compliant files from this information and delivers these to the two Global Data Assembly Centers (GDAC), where they are made publicly available. The user can access the data at either GDAC, cf. section “GDAC organization”.

The GDAC distributes the best copy of the data files. When a higher quality data file (e.g. calibrated data) is available, it replaces the previous version of the data file.

Archive of preliminary or real-time data is beyond the scope of the OceanSITES GDACs; this issue should be addressed by the long term archive policy for OceanSITES (under study).

## User Obligations

A user of OceanSITES data is expected to read and understand this manual and the documentation about the data as contained in the “attributes” of the NetCDF data files, as these contain essential information about data quality and accuracy.

A user of OceanSITES data must comply with the requirements set forth in the attributes “distribution_statement” and “citation” of the NetCDF data files.

Unless stated otherwise, a user must acknowledge use of OceanSITES data in all publications and products where such data are used, preferably with the following standard sentence:

“These data were collected and made freely available by the international OceanSITES project and the national programs that contribute to it.”

## Disclaimer

OceanSITES data are published without any warranty, express or implied.

The user assumes all risk arising from his/her use of OceanSITES data.

OceanSITES data are intended to be research-quality and include estimates of data quality and accuracy, but it is possible that these estimates or the data themselves contain errors.

It is the sole responsibility of the user to assess if the data are appropriate for his/her use, and to interpret the data, data quality, and data accuracy accordingly.

OceanSITES welcomes users to ask questions and report problems to the contact addresses listed in the data files or on the OceanSITES internet page.

## Further Information Sources and Contact Information:

- OceanSITES website: http://www.oceansites.org

- For further information about the benefits and distributing data onto the GTS, please refer to: http://www.jcommops.org/dbcp/gts or contact the OceanSITES Technical Coordinator - Hester Viola on projectoffice@oceansites.org.

- For information about unique numbering of OceanSITES Moorings and Gliders on the GTS see: http://www.wmo.int/pages/prog/amp/mmop/wmo-number-rules.html

# OceanSITES NetCDF data format version 1.1

OceanSITES uses the NetCDF (network Common Data Form) system, a set of software libraries and machine-independent data formats. Our implementation of NetCDF is based on the community-supported Climate and Forecast (CF) specification, which supplies a standard vocabulary and some metadata conventions.

OceanSITES layers several more conventions aboved the CF standard..  These are intended to make it easier to share in-situ data, to make it simpler for the GDACs to aggregate data from multiple sites,  and to ensure that the data can be created and understood by the basic NetCDF utilities.

- OceanSITES includes standard terms for the short name of both coordinate and data variables (measurements).

- File names are created using a standard, described in section 6.2.

- Coordinate variables, which describe the dimensions of a data set, are limited to a single set of longitude, latitude, depth and time (X,Y,Z, and T) dimensions in any single file. If data from a reference station cannot all be put on to a single set of axes, then separate files are created for these data.

An OceanSITES data file contains measurements such as temperature and salinity, continuously performed at different levels on a platform (e.g. mooring), as well as meteorological or other parameters recorded at the site, derived variables associated with the site, and complete location,  time, and provenance information.

The requirements are drawn almost exclusively from the NetCDF Style Guide:

- Units are compliant with CF/COARDS/Udunits ;

- The time parameter is encoded as recommended by COARDS and CF.

- Parameters are given standard names from the CF table

- Where time is specified as an attribute, the ISO8601 standard is used.

For more information on CF, COARDS, NetCDF, Udunits, and ISO8601 see:

- NetCDF: http://www.unidata.ucar.edu/software/netcdf/docs/BestPractices.html

- Udunits: http://www.unidata.ucar.edu/software/udunits/

- CF: http://cf-pcmdi.llnl.gov/

- COARDS: http://www.ferret.noaa.gov/noaa_coop/coop_cdf_profile.html

- ISO8601: http://en.wikipedia.org/wiki/ISO_8601

Note on format version

Since June 2008, the OceanSITES valid data format version is 1.1.
The User’s manual may be updated with clarifications, recommendations, additional optional attributes without changing the data format version.

## Data file dimensions

NetCDF dimensions provide information on the size of the data variables. OceanSITES allows a single parameter for each of the data dimensions, i.e. time, depth, latitude and longitude. Requirements are described further in the section on coordinate variables. Standard names for OceanSITES dimensions should be in upper case.

| Name | Example | Comment |
| --- | --- | --- |
| TIME | TIME=unlimited | Number of time steps. Example: for a mooring with one value per day and a mission length of one year, TIME contains 365 time steps. |
| DEPTH | DEPTH=5 | Number of depth levels. Example: for a mooring with measurements at 0.25, 10, 50, 100 and 200 meters, DEPTH=5. |
| LATITUDE | LATITUDE=1 | Dimension of the LATITUDE coordinate variable. Examples: for a mooring without positioning system, LATITUDE=1. For a mooring with a GPS receiver, use LATITUDE of the same dimension as TIME and provide the actual location. |
| LONGITUDE | LONGITUDE=1 | Dimension of the LONGITUDE coordinate variable. Examples: for a mooring without positioning system, LONGITUDE=1. For a mooring with a GPS receiver, use LONGITUDE of the same dimension as TIME and provide the actual location. |
| POSITION | POSITION=1 | Dimension of the POSITION_QC variable. |

Global attributes

The global attribute section of a NetCDF file contains metadata that describes the contents of the file overall, and allows for data discovery. All fields should be human-readable, and should be of character type, not numeric, even if the information content is a number. OceanSITES recommends that all of these attributes be used and contain meaningful information unless there are technical reasons rendering this impossible. However, files that do not at least contain the attributes listed as “mandatory” will not be considered OceanSITES-compliant. In OceanSITES, global attribute names are in lower-case letters.

Global attributes can be thought of as conveying five kinds of information:

- What: what are the data in this dataset;

- Where: the spatial coverage of the data;

- When: the temporal coverage of the data;

- Who: who produced the data;

- How: how were the data produced and made available.

The global attributes specification follows the recommendations of Unidata NetCDF Attribute Convention for Dataset Discovery, at :

http://www.unidata.ucar.edu/software/netcdf-java/formats/DataDiscoveryAttConvention.html

| Name | Example | Definition |
| --- | --- | --- |
| WHAT |  |  |
| data_type | data_type=”OceanSITES time-series data” | This field contains the type of data contained in the file. The list of acceptable data types is in reference table 1. Example: “OceanSITES time-series data”. This attribute is mandatory. |
| format_version | format_version=”1.1” | OceanSITES format version Example: “1.1”. This attribute is mandatory. |
| platform_code | platform_code=”CIS-1” | Platform unique code within OceanSITES project. Example: “CIS-1” mooring on CIS site (Central Irminger Sea). This attribute is mandatory. |
| date_update | date_update=”2006-04-11T08:35:00Z” | File update or creation date (UTC). See note on time format below. This attribute is mandatory. |
| institution | institution=”National Oceanographic Centre” | Specifies institution where the original data was produced. |
| site_code | site_code=”CIS” | Name of the site within OceanSITES project. Example: “CIS” for Central Irminger Sea. The site codes are available at : http://. |
| wmo_platform_code | wmo_platform_code=”48409” | WMO (World Meteorological Organization) identifier. This platform number is unique within the OceanSITES project. Example: “48409” for CIS-1 mooring. |
| source | source=”Mooring observation” | The method of production of the original data. For OceanSITES data, use one of the following: “Shipborne observation”, “Mooring observation” |
| history | history= “2005-04-11T08:35:00Z data collected, A. Meyer. 2005-04-12T10:11:00Z OceanSITES file with provisional data compiled and sent to DAC, A. Meyer.” | Provides an audit trail for modifications to the original data. It should contain a separate line for each modification, with each line beginning with a timestamp, and including user name, modification name, and modification arguments. The time stamp should follow the format outlined in the note on time formats below. |
| data_mode | data_mode=”R” | Indicates if the file contains real-time, provisional or delayed-mode data. The list of valid data modes is in reference table 5. |
| quality_control_indicator | Quality_control=”6” | Level of quality control applied to data. The values are listed in reference table 2.1. |
| quality_index | quality_index=”A” | A code value valid for the whole dataset: 0 unknown quality A excellent (no known problems, regular quality checking) B probably good (occasional problems, validation phase) C extremely suspect, frequent problems |
| references | references=”http:// www.oceansites.org, http://www.noc.soton.ac.uk/animate/index.php” | Published or web-based references that describe the data or methods used to produce it. Include a reference to OceanSITES and a project-specific reference if appropriate. |
| comment | comment=”…” | Miscellaneous information about the data or methods used to produce it. Any free-format text is appropriate. |
| Conventions | Conventions=”CF-1.4, OceanSITES 1.1” | Name of the conventions followed by the dataset. “convention” starting in lower case ‘c’ is still valid but will become obsolete. |
| Netcdf_version | netcdf_version=”3.5” | Netcdf version used for the data set |
| title summary | title=”CIS Mooring Data” summary=”Oceanographic mooring data from CIS observatory in the Central Irminger Sea, North Atlantic, in 2005. Measured properties: temperature and salinity at ten depth levels.” | Free-format text describing the dataset. The display of these two attributes together should allow data discovery for a human reader. “title”: title of the dataset. Use the file name if in doubt. “summary”: a longer description of the dataset. A paragraph of up to 100 words is appropriate. |
| naming_authority id | Naming_authority=”OceanSITES” id=”OS_CIS-1_200502_TS” | The “id” and “naming_authority” attributes are intended to provide a globally unique identification for each dataset. For OceanSITES data, use: naming_authority=”OceanSITES” and id=file name (without .nc suffix), which is designed to be unique. |
| cdm_data_type | cdm_data_type=”Station” | The “cdm_data_type” attribute gives the Unidata CDM (common data model) data type used by THREDDS. E.g. “Point”, “Trajectory”, “Station”, “Radial”, “Grid”, “Swath”. Use “Station” for OceanSITES mooring data. More: http://www.unidata.ucar.edu/projects/THREDDS/CDM/CDM-TDS.htm |
| WHERE |  |  |
| area | area=”North Atlantic Ocean” | Geographical coverage. Try to compose of the following: North/Tropical/South Atlantic/Pacific/Indian Ocean, Southern Ocean, Arctic Ocean. For specific sea area, use the International Hydrographic Bureau sea areas available at : http://vocab.ndg.nerc.ac.uk/client/vocabServer.jsp. |
| geospatial_lat_min | geospatial_lat_min=”59.8” | The southernmost latitude, a value between -90 and 90 degrees. |
| geospatial_lat_max | geospatial_lat_max=”59.8” | The northernmost latitude, a value between -90 and 90 degrees. |
| geospatial_lon_min | geospatial_lon_min=”-41.2” | The westernmost longitude, a value between -180 and 180 degrees. |
| geospatial_lon_max | geospatial_lon_max=”-41.2” | The easternmost longitude, a value between -180 and 180 degrees. |
| geospatial_vertical_min | geospatial_vertical_min=”10.0” | Minimum depth for measurements |
| geospatial_vertical_max | geospatial_vertical_max=”2000” | Maximum depth for measurements |
| WHEN |  |  |
| time_coverage_start | time_coverage_start=”2006-03-01T00:00:00Z” | Start date of the data in UTC. See note on time format below. |
| time_coverage_end | time_coverage_end=”2006-03-05T23:59:29Z” | Final date of the data in UTC. See note on time format below. |
| WHO |  |  |
| institution_references | institution_references=”http://www.nocs.uk” | References to data provider institution, the place to find all information on the dataset (web-based, i.e. give URLs). |
| contact | contact=”codac@nocs.uk” | Contact person’s e-mail. |
| author | author=”John Smith” | Name of the person responsible for the creation of the dataset. |
| data_assembly_center | data_assembly_center=”EUROSITES” | Data Assembly Center (DAC) in charge of this data file. The data_assembly_center are listed in reference table 4. |
| pi_name | pi_name=”Alice Juarez” | Name of the principal investigator in charge of the platform. |
| HOW |  |  |
| distribution_statement | distribution_statement=”Follows CLIVAR (Climate Varibility and Predictability) standards, cf. http://www.clivar.org/data/data_policy.php. Data available free of charge. User assumes all risk for use of data. User must display citation in any publication or product using data. User must contact PI prior to any commercial use of data.” | Statement describing data distribution policy. OceanSITES has adopted the CLIVAR data policy, which explicitly calls for free and unrestricted data exchange. Details at: http://www.clivar.org/data/data_policy.php |
| citation | citation=”These data were collected and made freely available by the OceanSITES project and the national programs that contribute to it.” | The citation to be used in publications using the dataset. |
| update_interval | update_interval=”daily” | Update interval for the file, one of the following: “hourly”, “daily”, “yearly”, “void”. Use “void” for delayed-mode or archive data that do not need continuous updating. |
| qc_manual | qc_manual=”OceanSITES User’s Manual v1.1” | This field contains the name of the manual that describes the quality control procedure. As of now, there is no separate QC manual, so the user’s manual is the appropriate reference. |

Note on time formats

Whenever time information is given in the global attributes, it ought to be a string of the format:

"YYYY-MM-DDThh:mm:ssZ" (i.e. year - month - day T hour : minute : second Z)

If higher resolution than seconds is needed, any number of decimal digits (“.s”) for the seconds is acceptable:

"YYYY-MM-DDThh:mm:ss.sZ"

In any case, the time must be in UTC. A capital “T” separates the date and the hour information. The string must end with a capital “Z”, an old indication of UTC. These formats are two (of many) described by ISO8601.

Examples:

- 2005-10-24T08:00:00Z

- 2008-01-01T22:50:02.031Z

## Variables

NetCDF variables include data measured by instruments, parameters derived from the primary measurements,  and coordinate variables, which may be nominal values, such as values for depth for instruments that do not directly record depth.  The variable names are written in CAPITALIZED letters. Each variable has a specific set of attributes, some of which are mandatory.

### Coordinate variables

The coordinate variables orient the data in time and space. For this purpose, they have an “axis” attribute defining that they point in X, Y, Z, and T dimensions. The DEPTH variable may be positive in either upward or downward direction, which is defined in its “positive” attribute.

All attributes in this section except the “comment” are mandatory; however “QC_indicator” may be omitted for any parameter if there is a separate QC variable for that parameter.

Optionally, the Z axis may be represented as pressure, if, for example pressure is recorded directly by an instrument and the calculation of depth from pressure would cause a loss of information. Depth is strongly preferred, since it allows data to be used more directly; data with different coordinate variables must be recorded in separate files.

| Type, Name, Dimension, Attributes | Comment |
| --- | --- |
| Double TIME(TIME); TIME:long_name = “time”; TIME:standard_name = “time”; TIME:units = “days since 1950-01-01T00:00:00Z”; TIME:_FillValue = 999999.0; TIME:_FillValue = 999999.0; TIME:valid_min = 0.0; TIME:valid_max = 90000.0; TIME:QC_indicator = <X>; TIME:QC_procedure = <Y>; TIME:uncertainty = <Z>; TIME:comment = “Optional comment...” TIME:axis = “T”; | Date and time (UTC) of the measurement in days since midnight, 1950-01-01. Example: Noon, Jan 2, 1950 is stored as 1.5. July 25, 2001, 19:14:00 is stored as 18833.8013889885. <X>: Replaces TIME_QC if constant. Cf. note on quality control in data variable section, value from reference table 2. <Y>: Cf. note on quality control in data variable section, value from reference table 2.1. <Z>: Choose appropriate value. |
| Float LATITUDE(LATITUDE); LATITUDE:long_name = “Latitude of each location”; LATITUDE:standard_name = “latitude”; LATITUDE:units = “degrees_north”; LATITUDE:_FillValue = 99999.0; LATITUDE:valid_min = -90.0; LATITUDE:valid_max = 90.0; LATITUDE:QC_indicator = <X>; LATITUDE:QC_procedure= <Y>; LATITUDE:uncertainty = <Z>; LATITUDE:comment = “Optional comment...” LATITUDE:axis=”Y”; | Latitude of the measurements. Units: degrees north; southern latitudes are negative. Example: 44.4991 for 44° 29’ 56.76’’ N <X>: Replaces POSITION_QC if constant. Cf. note on quality control in data variable section, value from reference table 2. <Y>: Cf. note on quality control in data variable section, value from reference table 2.1. <Z>: Choose appropriate value. |
| Float LONGITUDE(LONGITUDE); LONGITUDE:long_name = “Longitude of each location”; LONGITUDE:standard_name = “longitude”; LONGITUDE:units = “degrees_east”; LONGITUDE:_FillValue = 99999.0; LONGITUDE:valid_min = -180.0; LONGITUDE:valid_max = 180.0; LONGITUDE:QC_indicator = <X>; LONGITUDE:QC_procedure = <Y>; LONGITUDE:uncertainty = <Z>; LONGITUDE:comment = “Optional comment...” LONGITUDE:axis=”X”; | Longitude of the measurements. Unit: degrees east; western latitudes are negative. Example: 16.7222 for 16° 43’ 19.92’’ E <X>: Replaces POSITION_QC if constant. Cf. note on quality control in data variable section, value from reference table 2. <Y>: Cf. note on quality control in data variable section, value from reference table 2.1. <Z>: Choose appropriate value. |
| Float DEPTH(DEPTH); DEPTH:long_name = “Depth of each measurement”; DEPTH:standard_name = “depth”; DEPTH:units = “meters”; DEPTH:positive = “down”; DEPTH:_FillValue = -99999.0; DEPTH:valid_min = 0.0; DEPTH:valid_max = 12000.0; DEPTH:QC_indicator = <X>; DEPTH:QC_procedure = <Y>; DEPTH:uncertainty = <Z>; DEPTH:comment = “Optional comment...” DEPTH:axis=”Z”; DEPTH:reference=<R>; | Depth of each measurement. Example: 513 for a measurement 513 meters below sea surface. Z axes may be positive=”up” (atmospheric) or positive=”down” (oceanic). <X>: Replaces DEPTH_QC if constant. Cf. note on quality control in data variable section, value from reference table 2. <Y>: Cf. note on quality control in data variable section, value from reference table 2.1. <Z>: Choose appropriate value. <R> : The depth reference default value is “sea_level”. Other possible values are : “mean_sea_level”, “mean_lower_low_water”, “wgs84_geoid” DEPTH is mandatory for a mooring line. For instruments that do not have fixed depths such as Profiling floats, CTD, gliders, DEPTH is not required. |

Note on latitude and longitude WGS84 datum

The latitude and longitude datum is WGS84. This is the default output of GPS systems.

Note on handling observations in multiple locatiions

An OceanSITES files may contain observations performed in different locations. In that case, the TIME, LATITUDE and LONGITUDE dimensions have the same value.

For example: two CTD casts performed in different locations.

- TIME, LATITUDE and LONGITUDE dimensions are set to 2

- TIME(1) is the time of the first CTD cast, TIME(2) is the time of the second CTD cast

- LATITUDE(1) is the latitude of the first CTD cast, LATITUDE(2) is the latitude of the second CTD cast

- LONGITUDE(1) is the longitude of the first CTD cast, LONGITUDE(2) is the longitude of the second CTD cast

Note on TIME

By default, the time word represents the center of the data sample or averaging period. In all other cases the relationship between the time word and the sample or average period should be provided as a variable attribute: i.e. <param>:time_reference:”end”  or  “start” “last 10 minutes”

### Coordinate quality control variables

The coordinate variables have the same quality control variables as the data variables. If the quality control values are constant, the information is given in attributes of the coordinate variables. For details, see <PARAM>_QC in the section on data variables, and the note on quality control therein.

| Type, Name, Dimension, Attributes | Comment |
| --- | --- |
| Byte TIME_QC(TIME); | Quality flag for each TIME value. |
| Byte POSITION_QC(POSITION); | Quality flag for each LATITUDE and LONGITUDE value. |
| Byte DEPTH_QC(DEPTH); | Quality flag for each DEPTH value. |

Data variables

Data variables contain the actual measurements and indicators about their quality, uncertainty, and mode through which they were obtained. There are different options as to how the indicators are specified, whether in attributes or separate variables, which are outlined in the notes below the table. The variable names are standardized in reference table 3; replace <PARAM> with any of the names indicated there. Mandatory attributes are marked as such, however, OceanSITES requests that all other attributes be used and contain meaningful information unless technical reasons make this impossible.

| Type, Name, Dimension, Attributes | Comment |
| --- | --- |
| Float <PARAM>(TIME, DEPTH); <PARAM>:standard_name = “<X>”; <PARAM>:units = “<Y>”; <PARAM>:_FillValue = <Y>; <PARAM>:long_name = “Y”; <PARAM>:QC_indicator = <X>; <PARAM>:QC_procedure = <X>; <PARAM>:valid_min = <Y>; <PARAM>:valid_max = <Y>; <PARAM>:comment = “<Y>”; <PARAM>:sensor_depth = <Y>; <PARAM>:sensor_mount = <X>; <PARAM>:sensor_orientation = <X>; <PARAM>:sensor_name = <Y>; <PARAM>:sensor_serial_number = <Y>; <PARAM>:ancillary_variables = “<Y>” ; <PARAM>:uncertainty = <Y>; <PARAM>:accuracy = <Y>; <PARAM>:precision = <Y>; <PARAM>:resolution = <Y>; <PARAM>: cell_methods = “<X>”; <PARAM>:DM_indicator = “<X>” <PARAM>:reference_scale = “<Y>” | <PARAM> names are defined in reference table 3. Examples: TEMP, PSAL, DOXY. These 3 attributes are mandatory: standard_name, units and _FillValue. These 11 attributes are highly desirables : QC_indicator, QC_procedure, valid_min, valid_max, sensor_name, uncertainty sensor_serial_number accuracy, precision, resolution, DM_indicator. The other attributes are optional. <X> : standardized attributes listed in reference tables <Y> : attributes whose value is set by the PI (Principal Investigator) standard_name: type char, see reference. table 3 units: type char, see reference table 3 _FillValue: type float, see reference table 3 long_name: type char, free text QC_indicator: type byte, see reference table 2 and note on quality control below QC_procedure type byte, see reference table 2.1 and note on quality control below valid_min: type float. Minimum value for valid data valid_max: type float. Maximum value for valid data comment. type char. Any free-format text with comments as appropriate. sensor_depth. type float. Nominal sensor depth(s) in meters, counting positive as per DEPTH:positive. sensor_mount type char. See reference table 7 for sensor mounting characteristics. sensor_orientation type char. See reference table 8 for sensor orientation characteristics. sensor_name type char (if the data all come from a single sensor). sensor_serial_number type char (if the data all come from a single sensor). ancillary_variables. type char. Other variables associated with <PARAM>, e.g. <PARAM>_QC. List as space-separated string. Example: TEMP:ancillary_variables=”TEMP_QC TEMP_DM TEMP_UNCERTAINTY” uncertainty: type float. Overall measurement uncertainty, if constant. Cf. note on uncertainty below. accuracy: type float. Nominal sensor accuracy. Cf. note on uncertainty below. precision: type float. Nominal sensor precision. Cf. note on uncertainty below. resolution: type float. Nominal resolution of this data parameter. cell_methods: type char. Specifies cell method as per CF convention. Example: TEMP:cell_methods=”TIME: point DEPTH: point LATITUDE: point LONGITUDE: point” Values are listed in table 2.2 DM_indicator: Type char. Data mode, if constant, as per reference table 5. Cf. note on data modes below. reference_scale: type char. For some measurements that are provided according to a standard reference scale specify the the reference scale with this optional attribute. Example: ITS-90, PSS-78 |
| Byte <PARAM>_QC(TIME, DEPTH); <PARAM>_QC:long_name = “quality flag”; <PARAM>_QC:conventions = “OceanSITES reference table 2”; <PARAM>_QC:_FillValue = -128; <PARAM>_QC:valid_min = 0; <PARAM>_QC:valid_max= 9; <PARAM>_QC:flag_values = 0, 1, 2, 3, 4, 5, 7, 8, 9; <PARAM>_QC:flag_meanings = “no_qc_performed good_data probably_good_data bad_data_that_are_potentially_correctable bad_data value_changed not_used nominal_value interpolated_value missing_value” | Quality flags for values of associated <PARAM>. The flag scale is specified in reference table 2, and is included in the flag_meanings attribute. long_name: type char. fixed value conventions. type char. Required; fixed value _FillValue. type byte. Required; fixed value valid_min. type byte. Required; fixed value valid_max: type byte. Required; fixed value flag_values: type byte. Required; fixed value flag_meanings: type char. Required; fixed value |
| Char <PARAM>_DM(TIME, DEPTH); <PARAM>_DM:long_name = “method of data processing “; <PARAM>_DM:conventions = “ OceanSITES reference table 5”; <PARAM>_DM:flag_values = “R”, “P”, “D”, “M”; <PARAM>_DM:flag_meanings = “real-time provisional delayed-mode mixed”; <PARAM>_DM:_FillValue = “ “; | This is the data mode. Indicates if the data point is real-time, delayed-mode or provisional mode. It is included when the dataset mixes modes for a single variable. See note on data modes below, and reference table 5. long_name: type char. Required; fixed value conventions: type char. Required; fixed value flag_values: type char. Required; fixed value flag_meanings: type char. Required; fixed value _FillValue: type char. Required; fixed value |
| Float <PARAM>_UNCERTAINTY(TIME, DEPTH): <PARAM>_UNCERTAINTY:long_name = “uncertainty” <PARAM>_UNCERTAINTY:_FillValue=<Y> <PARAM>:units = “<Y>”; | Overall uncertainty of the data given in <PARAM>. See note on uncertainty below. long_name: type char. Required; fixed value _FillValue: type float. Required. units: type char. Required. Must be the same as <PARAM>:units. |

Note on quality control (QC)

The quality of the data in a variable <PARAM> is described by the attribute <PARAM>:QC_procedure, and one of the following: the attribute <PARAM>:QC_indicator or the variable <PARAM_QC>.

<PARAM>:QC_procedure is mandatory and contains values from reference table 2.1, which describe what kind of quality control procedure has been applied.

It is mandatory to define one of <PARAM>:QC_indicator or <PARAM_QC>, both of which would contain values describing the data quality as per reference table 2. If the quality is the same for all <PARAM>, use <PARAM>:QC_indicator. Else, use <PARAM_QC>.

Note on uncertainty

If the overall measurement uncertainty for a variable <PARAM> is reasonably well-known, it must be provided in the attribute <PARAM>:uncertainty if it is constant, or in a variable of its own, <PARAM>_UNCERTAINTY, if it is not constant. If uncertainty is given in either way, the attribute <PARAM>:accuracy is optional.
If it is impossible to estimate the overall measurement uncertainty, it is required to define at least the attribute <PARAM>:accuracy with the nominal sensor accuracy.
The attributes <PARAM>:precision and <PARAM>:resolution are optional; they contain the sensor precision and resolution if defined.

Note on data modes (DM)

Data mode may be represented as a global attribute “data_mode” if all data is a single mode, or as an attribute to a variable <PARAM>:DM_indicator if all data for <PARAM> is in a single mode. If a parameter contains a mixture of modes, these attributes should be set to “M” and the actual data modes should be represented by an extra variable, <PARAM>_DM. The values for the data modes are explained in reference table 5.

Example for sea temperature measurements and associated quality flags

Float TEMP(TIME, DEPTH);

TEMP:long_name = “sea water temperature in-situ ITS-90 scale”;

TEMP:standard_name = “sea_water_temperature”;

TEMP:units = “degree_Celsius”;

TEMP:_FillValue = 99999.f;

TEMP:QC_indicator = 1;

TEMP:valid_min = -2.0f;

TEMP:valid_max = 40.f;

TEMP:comment = “”;

TEMP:ancillary_variables = “TEMP_QC” ;

TEMP:resolution = 0.001f;

TEMP:uncertainty = 0.01f;

TEMP:error = 0.02f;

TEMP:cell_methods=”TIME: point DEPTH: point LATITUDE: point

LONGITUDE: point”;TEMP:DM_indicator=”P”;

TEMP:reference_scale = “ITS-90”;

TEMP_QC:long_name = “quality flag”;

TEMP_QC:conventions = “OceanSITES reference table 2”;

TEMP_QC:flag_values = 0, 1, 2, 3, 4, 5, 7, 8, 9;

TEMP_QC:flag_meanings = “no_qc_performed good_data probably_good_data bad_data_that_are_potentially_correctable bad_data value_changed not_used nominal_value interpolated_value missing_value”

TEMP_QC:_FillValue = 0;

# OceanSITES metadata format

For each data file, an OceanSITES metadata file should be available.

The OceanSITES metadata file is a text document that contains all the attributes defined in the NetCDF file as well as more detailed information on sensors. This may be provided as a Word document, a modified CDL (NetCDF output) file, or a free-form text file.

The OceanSITES data management team is developing an OGC-SensorML metadata format.

The list of required metadata is:

- All metadata present in the global attribute section of the data file

- All metadata present in the additional metadata tables

#### OceanSITES platform information

| Name | Value | Required/ Optional |
| --- | --- | --- |
| platform_category | Air-Sea Flux Site, Transport Site, Physical, Meteorological, Biogeochemical, Geophysical | Required |
| wmo_message_format | WMO standard formats: FM13, FM18, FM64, or FM65. PIs may request desired WMO formats and GDAC will determine the final formats to be used | Optional |
| Wind_direction_conventions | WMO standard uses wind-from-direction, indicate if the real-time wind direction received by GDAC/DAC is a wind-to-direction before GTS dissemination. | Optional |
| platform_message_reporting_frequency | The frequency of message reporting from buoy to DAC, such as daily, hourly, or every 10min etc.) | Required |

#### OceanSITES Parameter and Sensor Information

This section is to be used by PI to provide parameter and associated sensor information for each of the platform dataset files specified in section 2. If real-time GPS tracking data are available, use LATITUDE and LONGITUDE as the position parameters. Please use one form for each parameter.

| Name | Value | Required Optional |
| --- | --- | --- |
| parameter_name | OS 1.1 parameter - valid parameter name in OceanSITES parameter dictionary as netCDF variable name Example : TEMP | Required |
| sensor_vendor | Name of the sensor vendor Example : PMEL | Desired |
| sensor_sampling_period | Period(s) in minutes when sampling occurs in one message report from buoys, typically in one hour Example : Instantaneous | Desired |
| sensor_sampling_frequency | Instantaneous or frequency in HZ or every 15 second etc Example : 1 per 10 min | Desired |
| sensor_reporting_time | UTC time represents middle, beginning, or end of sampling periods, indicate if sensor reporting time differs from the corresponding platform message reporting time Example: Sensor reports at the top of the hour and every ten minutes after. Data is transmitted once daily as a mean. | Optional |

# Reference tables

## Reference tables 1: data type and data code

### Reference table 1: Data type

The data_type global attribute should have one of the valid values listed here.

Data type

OceanSITES metadata

OceanSITES profile data

OceanSITES time-series data

OceanSITES trajectory data

Reference table 2: Variable quality control flag scale

The quality control flags indicate the data quality of the data values in a file, and are normally assigned after quality control procedures have been performed. These codes are used in the <PARAM>_QC variables to describe the quality of each measurement, or  in the attribute <PARAM>:QC_indicator to describe the overall quality of the parameter.

| Code | Meaning | Real-time comment | Delayed-mode comment |
| --- | --- | --- | --- |
| 0 | No QC was performed | - | - |
| 1 | Good data | All real-time QC tests passed. | All delayed-mode tests passed. |
| 2 | Probably good data | - | - |
| 3 | Bad data that are potentially correctable | These data are not to be used without scientific correction. | Possible re-calibration needed. |
| 4 | Bad data | Data have failed one or more tests. | Data have failed one or more tests. |
| 5 | Value changed | Data may be recovered after transmission error. | - |
| 6 | Not used | - | - |
| 7 | Nominal value | Data were not observed but reported; i.e. an anchor drop position or an instrument target depth, as opposed to a GPS position time series or a pressure sensor time series. | - |
| 8 | Interpolated value | Missing data may be interpolated from neighbouring data in space or time. | - |
| 9 | Missing value | - | - |

Reference table 2.1: Overall quality control procedure indicator

This table describes the quality procedures applied to all the measurement of a parameter.
These values are used as an overall quality indicator (i.e. one summarizing all measurements) in the attributes of each variable <PARAM>.

Cf. <PARAM>:QC_procedure attribute description in section 3.2.3.

| Code | Meaning |
| --- | --- |
| 0 | No QC performed |
| 1 | Ranges applied, bad data flagged |
| 2 | Data interpolated |
| 3 | Sensor malfunctioning (data possibly useful) |
| 4 | Data missing |
| 5 | Data manually reviewed |
| 6 | Data verified against model or other contextual information |
| 7 | Other QC process applied |

### Reference table 2.2: cell methods

From NetCDF Climate and Forecast (CF) Metadata Conventions, Version 1.2, 4 May, 2008

In the Units column, u indicates the units of the physical quantity before the method is applied.

| Cell Method | Units | Description |
| --- | --- | --- |
| point | u | The data values are representative of points in space or time (instantaneous). |
| sum | u | The data values are representative of a sum or accumulation over the cell. |
| maximum | u | Maximum |
| median | u | Median |
| mid_range | u | Average of maximum and minimum |
| minimum | u | Minimum |
| mean | u | Mean (average value) |
| mode | u | Mode (most common value) |
| standard_deviation | u | Standard deviation |
| variance | u2 | Variance |

## Reference table 3: OceanSITES parameter dictionary

### Convention for parameter names, standard names and units

The parameter dictionary is now contained in an Excel file, which is available at http://www.oceansites.org/parameters/...

- Parameter names should start with a 4 characters code based on SeaDataNet-BODC parameter discovery vocabulary.
They are not strictly standardized, however.
When necessary, a parameter name has a suffix that designates secondary parameters. The suffix starts with the character “_”.

The NetCDF “standard_name” attribute contains the standardized parameter name from CF conventions.

The NetCDF “units” attribute are compliant with Udunits as implemented in the CF/COARDS standards.

As the parameter names are not strictly standardized, one should use the standard_name attribute to query a particular measurement from different data files.

Example
On a mooring, sea temperature measured by a series of Microcat CTD is reported as TEMP, with a standard name of SEA_WATER_TEMPERATURE.

Secondary temperature measurement performed by an oxygen sensor is reported as TEMP_DOXY with a standard name of temperature_of_sensor_for_oxygen_in_sea_water.

For both measurements, the unit attribute is “degree_Celsius”.

### References

The OceanSITES standard names are taken from the CF standard names, available at:

http://cf-pcmdi.llnl.gov/documents/cf-standard-names/

The parameter names are based on SeaDataNet-BODC parameter discovery vocabulary available at:

http://seadatanet.maris2.nl/v_bodc_vocab/welcome.aspx
Select P021, “ BODC Parameter Discovery Vocabulary”

The units are compliant with Udunits, as implemented by the CF standard; definitions are available at:

http://www.unidata.ucar.edu/software/udunits

The valid parameter names, standard names, long_names and units are available at:

- http://...

The following list an extract of the OceanSITES parameter dictionary for parameter name and standard name.

| Parameter | Standard name | Type of data |
| --- | --- | --- |
| AIRT | air_temperature | M |
| ATMP | air_pressure | M |
| ATMS | air_pressure_at_sea_level | M |
| CDIR | direction_of_sea_water_velocity was sea_water_direction | V |
| CNDC | sea_water_electrical_conductivity | H |
| CSPD | sea_water_speed | H |
| DEPTH | depth | H |
| DEWT | dew_point_temperature | M |
| DOX2 | moles_of_oxygen_per_unit_mass_in_sea_water was dissolved_oxygen | H |
| DOXY | mass_concentration_of_oxygen_in_sea_water was dissolved_oxygen | H |
| DOXY_TEMP | temperature_of_sensor_for_oxygen_in_sea_water | H |
| DRYT | dry_bulb_temperature | M |
| DYNHT | dynamic_height | H |
| EWCT | eastward_sea_water_velocity | V |
| FLU2 | fluorescence | H |
| HCSP | sea_water_speed |  |
| HEAT | heat_content | H |
| ISO17 | isotherm_depth | H |
| LW | surface_downwelling_longwave_flux_in_air | F |
| NSCT | northward_sea_water_velocity | V |
| OPBS | optical_backscattering_coefficient | O |
| PCO2 | surface_partial_pressure_of_carbon_dioxide_in_air was CO2_partial_pressure_in_dry/wet_gas | H |
| PRES | sea_water_pressure | H |
| PSAL | sea_water_salinity | H |
| RAIN | rainfall_rate | M |
| RAIT | thickness_of_rainfall_amount | M |
| RELH | relative_humidity | M |
| SDFA | surface_downwelling_shortwave_flux_in_air | F |
| SRAD | isotropic_shortwave_radiance_in_air | M |
| SW | surface_downwelling_shortwave_flux_in_air | F |
| TEMP | sea_water_temperature | H |
| UCUR | eastward_sea_water_velocity | V |
| UWND | eastward_wind | M |
| VAVH | sea_surface_wave_significant_height | W |
| VAVT | sea_surface_wave_zero_upcrossing_period | W |
| VCUR | northward_sea_water_velocity | V |
| VDEN | sea_surface_wave_variance_spectral_density | W |
| VDIR | sea_surface_wave_from_direction | W |
| VWND | northward_wind | M |
| WDIR | wind_to_direction | M |
| WSPD | wind_speed | M |

## Reference table 4: Data Assembly Center Codes

| Data Assembly Centers and institutions |
| --- |
| EUROSITES | EuroSites EU project |
| JAMSTEC | Jamstec, Japan |
| MEDS | MEDS, Canada |
| NDBC | National Data Buoy Center, USA |
| NOCS | National Oceanography Centre, Southampton |
| PMEL | PMEL, USA |
| SIO | SIO, Scripps, USA |
| WHOI | Woods Hole Oceanographic Institution, USA |
| INCOIS | Indian National Centre for Ocean Information Services |
| MBARI | Monterey Bay Aquarium Research Institute |
| CCHDO | CLIVAR and Carbon Hydographic Office |

Reference table 5: data mode

The values for the variables “<PARAM>_DM”, the global attribute “data_mode”, and variable attributes “<PARAM>:DM_indicator” are defined as follows:

| Value | Meaning |
| --- | --- |
| “R” | Real-time data. Data coming from the (typically remote) platform through a communication channel without physical access to the instruments, disassembly or recovery of the platform. Example: for a mooring with a radio communication, this would be data obtained through the radio. |
| “P” | Provisional data. Data obtained after the instruments or the platform have been recovered or serviced. Example: for instruments on a mooring, this would be data downloaded directly from the instruments after the mooring has been recovered on a ship.. |
| “D” | Delayed-mode data. Data published after all calibrations and quality control procedures have been applied on the internally recorded or best available original data. This is the best possible version of processed data. |
| “M” | Mixed. This value is only allowed in the global attribute “data_mode” or in attributes to variables in the form “<PARAM>:DM_indicator”. It indicates that the file contains data in more than one of the above states. In this case, the variable(s) <PARAM>_DM specify which data is in which data mode. |

## Reference table 6: OceanSITES sites catalog

The OceanSITES catalogue is managed by the technical coordinator (email : xxx@jcomm).

An OceanSITES site has a unique name provided by OceanSITES technical coordinator after agreement of the OceanSITES board.

The technical coordinator ensures that platform_codes are unique among OceanSITES.

The WMO codes are requested to WMO by the DAC or the national contact with WMO.

The OceanSITES sites catalogue is available at

http://www.oceansites.org/....

The following list is an extract from the catalogue.

Hester : revisit the list please.

| OceanSITES moorings catalogue based on data files available from GDAC |
| --- |
| site code | platform code | WMO code | DAC | contact |
| CIS | CIS-1 | 44478 | EuroSITES | NOCS |
| CIS | CIS-2 | 44478 | EuroSITES | NOCS |
| ESTOC | ESTOC-1 | 13471 | EuroSITES | NOCS |
| PAP | PAP-1 | 62442 | EuroSITES | NOCS |
| PAP | PAP-2 | 62442 | EuroSITES | NOCS |
| BTM | BTM | - | NDBC ? | UCSB |
| KEO | KEO32N145E | 28401 | PMEL | Cronin |
| MOVE | V404 | 41173 | NDBC ? | SIO |
| MOVE | V405 | - | NDBC ? | SIO |
| MOVE | V406 | 41174 | NDBC ? | SIO |
| NTAS | NTAS | - | NDBC ? | Woods Hole |
| STRATUS | STRATUS | - | NDBC ? | Woods Hole |
| TAO | 0n110w | 32323 | PMEL | McPhaden |
| TAO | 0n140w | 51311 | PMEL | McPhaden |
| TAO | 0n165e | 52321 | PMEL | McPhaden |
| TAO | 0n170w | 51010 | PMEL | McPhaden |
| PIRATA | 0n23w | 15004 | PMEL | McPhaden |
| RAMA | 0n80.5e | 23001 | PMEL | McPhaden |
| PIRATA | 10s10w | 15001 | PMEL | McPhaden |
| PIRATA | 15n38w | 13008 | PMEL | McPhaden |

## Reference table 7: sensor mount characteristics

The <PARAM>:”sensor_mount” attribute indicates the way a sensor is mounted on a mooring.

The following table lists the valid sensor_mount attribute values.

| sensor_mount | comment |
| --- | --- |
| mounted_on_fixed_structure |  |
| mounted_on_surface_buoy |  |
| mounted_on_mooring_line |  |
| mounted_on_bottom_lander |  |
| mounted_on_moored_profiler |  |
| mounted_on_glider |  |
| mounted_on_shipborne_fixed |  |
| mounted_on_shipborne_profiler |  |
| mounted_on_seafloor_structure |  |
| mounted_on_benthic_node |  |
| mounted_on_benthic_crawler |  |
| mounted_on_surface_buoy_tether |  |
| mounted_on_seafloor_structure_riser |  |
| mounted_on_fixed_subsurface_vertical_profiler |  |

## Reference table 8: sensor orientation characteristics

When appropriate, the <PARAM>:”sensor_orientation” attribute indicates the way a sensor is oriented on a mooring.

The following table lists the valid sensor_orientation attribute values.

| sensor_orientation | comment |
| --- | --- |
| downward | Example : ADCP measuring from surface to bottom currents. |
| upward | Example : In-line ADCP measuring currents towards the surface |
| vertical | Example : ??? |
| horizontal | Example : ??? |

# GDAC organization

There are two GDACs (global data assembly centers) for redundancy, which are the users’ access points for OceanSITES data. One GDAC is located in France (Coriolis, http://www.coriolis.eu.org), the other one in the USA (NDBC, National Data Buoy Center, http://www.ndbc.noaa.gov). The GDACs handle OceanSITES data, metadata, and index files on ftp servers. The servers at both GDACs are synchronized at least daily to provide the same OceanSITES data.

The user can access the data at either GDAC’s ftp site:

- ftp://ftp.ifremer.fr/ifremer/oceansites

- ftp://data.ndbc.noaa.gov/data/oceansites

From these root directories of the GDACs downward, the organization of the directories and files is:

site/platform/FileName.nc

- site: OceanSites site code

- platform: platform code

The sites and platform codes are available in the “OceanSITES catalogue” document at either GDAC’s root directory:

- oceansites_catalogue.xml

## File naming convention

The OceanSITES file names use the following naming convention for data and metadata files.

### Data file naming convention

OS_XXX_YYY_T_PARTX.nc

- OS - OceanSITES prefix

- XXX - Platform code from the OceanSITES catalogue

- YYY - Deployment code (unique code for deployment - date or number)

- T - Data Mode

  - R: real-time data

  - P : provisional data

  - D: delayed mode

  - M: mixed delayed mode and real-time.

- <PARTX> - User defined field for identification of data

Example

- OS_CIS-1_200905_R_CTD.nc

This file contains temperature and salinity data from the CIS-1 mooring, from the EuroSITES project, for the deployment performed in May 2009.

### Metadata file naming convention

OS_XXX_YYY_META.zzz

- OS: OceanSITES prefix

- XXX: platform code

- YYY: deployment code

- zzz: metadata file suffix (.txt, .doc, .xml)

These metadata are for the corresponding data file(s) OS_XXX_YYY_T_ZZZ_PARTX.nc

Example

- OS_CIS-1_200905_META.xml

This file contains the metadata of CIS-1 mooring, for the deployment performed in May 2009.

## Index file for data files

To allow for data discovery without downloading the data files themselves, an index file is created at the GDAC level, which lists all available data files and the location and time ranges of their data contents:

- The data index file is located at the root directory of the GDAC.

- The index file contains the list and a description of all data files available on the GDAC.

- There is a header section, lines of which start with # characters.

- The information sections are comma-separated values.

- Each line contains the following information:

- FILE: the file name, beginning from the GDAC root directory

- DATE_UPDATE: the update date of the file, YYYY-MM-DDTHH:MI:SSZ

- START_DATE: first date for observations, YYYY-MM-DDTHH:MI:SSZ

- END_DATE: last date for observations, YYYY-MM-DDTHH:MI:SSZ

- SOUTHERN_MOST_LATITUDE

- NORTHERN_MOST_LATITUDE

- WESTERN_MOST_LONGITUDE

- EASTERN_MOST_LONGITUDE

- UPDATE_INTERVAL: M monthly, D daily, Y yearly, V void

- SIZE: the size of the file in megabytes

- GDAC_CREATION_DATE: date of creation of the file on the GDAC

- GDAC_UPDATE_DATE: date of update of the file on the GDAC.

- DATA_MODE: R, P, D, M (real-time, provisional, delayed mode, mixed; see reference table 5)

- PARAMETERS: list of parameters (standard_name) available in the file separated with blank

- The fill value is empty (eg. : ,,).

GDAC data files index: oceansites_files_index.txt

# OceanSites FTP GLOBAL INDEX # ftp://ftp.ifremer.fr/ifremer/oceansites # Contact: http://www.oceansites.org # Index update date YYYY-MM-DDTHH:MI:SSZ: 2008-03-30T18:37:46Z # #FILE,DATE_UPDATE,START_DATE,END_DATE, SOUTHERN_MOST_LATITUDE,NORTHERN_MOST_LATITUDE,WESTERN_MOST_LONGITUDE,EASTERN_MOST_LONGITUDE,UPDATE_INTERVAL,SIZE,GDAC_CREATION_DATE,GDAC_UPDATE_DATE,DATA_MODE,PARAMETERS TAO/0n170w/OS_0n170w_SW_LW_2m.nc,2008-04-12T08:05:00Z,2007-03-17T18:07:00Z,2008-04-12T08:05:00Z,0,0,-170,-170,M,16.7,2008-04-12T08:05:00Z,2008-04-12T08:05:00Z,R,sea_water_pressure sea_water_temperature sea_water_salinity

# Glossary, definitions

This chapter gives a definition for the OceanSITES items described in this manual.

## SITE

## PLATFORM

## DEPLOYMENT

# Comments

I don’t agree with this being mandatory

Don’t agree with mount/orientation being mandatory

Related to Matthias "Raw data?" transparent

If PI wants to archive RT data, they must do it themselves.

I think this is a more positive statement than calling them “restrictions”.

Change it to 1.2 when the manual is approved.

Should we mention how someone receives their platform_code?

TC : yes, I added this information on §5.6

This is a dynamic list that is available via the jcommops web site.  I suggest removing the table as this document cannot keep up to date with all the site_codes.

Again, mention that this code is received for a site once metadata is received and data are approved for ingest into the GDACs.

TC : see chapter 5.6

Nan, is the upper case necessary in the 'c' of Convention ?

I believe the standard is Conventions; CF is deciding on how to create a  multi-part convention statement.

Removing the fill value for time, lat, depth etc is counterproductive. There may be special cases (most positions known, some mising) where these are needed; they should be specified in the standard.

I don’t see how this is counterproductive. Coordinate variables should all have values, otherwise what sense does the data make that are gridded on these coordinates. I think that some NetCDF/COARDS/CF clients (such as Ferret) will fail to read a file with fill values – or non-monotonically increasing time axis or other duplicate coordinate values. These are pathological cses.

TC : yes, some of our programs fail in this case.

Removing the fill value for time, lat, depth etc is counterproductive. There may be special cases (most positions known, some mising) where these are needed; they should be specified in the standard.

See above

Default value is relative to sea level – this is true for almost all instruments on open ocean moorings

Does that answer to NG13 ?

Related to Matthias proposal “Geoid reference datum”

Please be sure this is consistent with the new  NetCDF best-practices for profiles/trajectories! ALSO, how would depth be handled?

Mount and orientation are not needed for many (most?) instruments!!!  Also, this is spelled out in the SML file

the file format checker will have to list the missing highly desirable parameters

Remark from TC and MP 21/01/2009 : the sensor_depth attribute is a duplicate of DEPTH. As it is not mandatory, I would not use it. Moreover, sensor_depth is described as a float in the manual, but here we have an array of floats (which cannot be set in a single float).

This is needed for ADCPs, for example, where bin data has depth but instrument depth is interesting (and different!)

These are the only attributes that refer to a physical sensor. Some variables in a data set may be produced by several instruments.  It’s O.K. to have a value for this attribute only if there is a one-to-one mapping.

should we list the items of the metadata form ?

We should also revisit the parameter names. Can include the parameter names in this file? It’s essential for one writing the NetCDF file to have both this document and the parameter table. Let’s make it a little easier by providing them together.

Please check that this term is in Udunits! I think this may not be correct??  degree_C

This name is a very poor choice!!!

I propose to remove this column as it is not used anymore in the file naming convention

O.K.  I see this table.  Should we also have the link to the Excel file?  Can we “collapse” the two together?

This is not my understanding of the definition of this term (Post-recovery) as discussed in Vienna.

What is the email contact with the coordinator (with no personal email) ?

related to Matthias transparent 1 : Bottom Pressure vs. in-line Pressure

isn’t it

need to differentiate between surface mooring line and subsurface mooring line???? Different dynamics, I think.

TC : isn’t it the difference between mounted_on_surface_buoy and mounted_on_mooring_line ?

related to “Bottom Pressure vs. in-line Pressure”

We could use a separate short name??? Check BODC names?

Please specify that this is only recommended for profilers? It is meaningless for temperature sensors and many current meters.

Do we keep that statement ? The sites-platform catalogue could be on the technical coordinator web site ?

Updated after Monday 7th of December teleconference meeting